## Slide 1
AN-NAJAH NATIONAL UNIVERSITY • COMPUTER NETWORK
Secure Home Dashboard
Docker + Tailscale + GNS3 + NAT
Rahaf Alyan
Tabark Mdena
Leen Akkawi
Supervisor: Dr. Jehad Hamamreh
GNS3
Docker
VPN
NAT

## Slide 2
Project Overview
Network Simulation
GNS3 topology with NAT1, Router R1, and Ubuntu VM connected in a real-world setup
Containerization
Heimdall dashboard deployed via Docker on port 8080, running on UbuntuDockerGuest-1
Secure VPN Access
Tailscale VPN provides encrypted remote access from anywhere using IP 100.90.203.89
NAT Configuration
Cisco IOS router R1 configured with NAT overload (PAT) for internet access on subnet 192.168.10.0/24

## Slide 3
Tools & Technologies
GNS3
v2.2.58.1
Network simulation and topology design
Docker
Latest
Container platform for Heimdall dashboard
Heimdall
linuxserver
Web-based home dashboard on port 8080
Tailscale
Latest
WireGuard-based secure VPN tunnel
Cisco IOS
12.4
Router R1 — NAT/PAT and routing config

## Slide 4
Network Topology
Internet
8.8.8.8
NAT1
192.168.122.1
Router R1
Fa0/0: .122.2
Fa0/1: .10.1
Ubuntu VM
192.168.10.2
192.168.122.0/24
192.168.10.0/24
Tailscale VPN: 100.90.203.89 | Dashboard URL: http://100.90.203.89:8080 | Local: http://localhost:8080
NAT overload (PAT) allows all 192.168.10.x devices to share R1 Fa0/0 public IP for internet access via GNS3 NAT1

## Slide 5
Router R1 — Configuration
Interface Setup
interface FastEthernet0/0
ip address 192.168.122.2
255.255.255.0
ip nat outside
no shutdown
!
interface FastEthernet0/1
ip address 192.168.10.1
255.255.255.0
ip nat inside
no shutdown
NAT & Routing
ip route 0.0.0.0 0.0.0.0
192.168.122.1
!
access-list 1 permit
192.168.10.0 0.0.0.255
!
ip nat inside source list 1
interface Fa0/0 overload
!
end
wr

## Slide 6
IP Addressing Table
Device | IP Address | Role / Notes
Host Machine (Tailscale) | 100.90.203.89 | VPN remote access IP
NAT1 — GNS3 Built-in | 192.168.122.1 | Internet gateway
R1 — Fa0/0 (outside) | 192.168.122.2 | ip nat outside
R1 — Fa0/1 (inside) | 192.168.10.1 | ip nat inside / Default GW
UbuntuDockerGuest-1 | 192.168.10.2 | Docker host + Heimdall :8080

## Slide 7
Connectivity Verification
Router sees NAT1
ping 192.168.122.1
SUCCESS
Ubuntu reaches Router
ping 192.168.10.1
SUCCESS
Internet connectivity
ping 8.8.8.8
SUCCESS
Dashboard local access
http://localhost:8080
SUCCESS
Remote VPN access
http://100.90.203.89:8080
SUCCESS

## Slide 8
Thank You
Secure Home Dashboard — Project Complete
GNS3 topology with full NAT/PAT on Cisco IOS router
Heimdall dashboard deployed via Docker container
Secure remote access via Tailscale VPN (WireGuard)
Full internet connectivity verified end-to-end
Team
Rahaf Alyan
Tabark Mdena
Leen Akkawi
Dr. Jehad Hamamreh
Supervisor
An-Najah National University
Computer Network • 2025-2026